## Slide 1
Network CLI Structured Parser
Standard Operating Procedure
Parsing · Health Checks · Compound Conditions · Reports · Collector
cisco_nxos · cisco_ios · TextFSM · TTP · YAML Checks

## Slide 2
Table of Contents
1. Overview & Architecture
2. Running the Parser
3. Directory Structure
4. Status Codes
5. Adding a New Command
6. TextFSM Templates
7. TTP Templates
8. Pipe-Filtered Commands
9. commands.yaml Reference
10. Report Generator Overview
11. Health Check Path Syntax
12. Conditions (14 total)
13. match: all vs any
14. Severity Levels
15. ★ AND Conditions (NEW)
16. ★ one_of / not_one_of (NEW)
17. ★ Branches IF/ELIF/ELSE (NEW)
18. ★ print Field (NEW)
19. Per-Device Overrides & Baseline
20. Delta · HTML Reports · Collector
★ = New features in this release

## Slide 3
Overview & Architecture
One JSON snapshot per device — every command, every output
Parser Chain (per command):
commands.yaml lookup
├── raw_only → skip parsing, preserve raw text
├── ntc → NTC Templates (ntc-templates library)
├── custom → Custom TextFSM template
├── ttp → TTP template
├── hierarchical → Python regex parser (multicast / VRF-nested)
└── auto_discover (unknown commands)
├── Step 1: NTC Templates (reconstructed command string)
├── Step 2: Convention TextFSM {platform}_{cmd}.textfsm
├── Step 3: Convention TTP {platform}_{cmd}.ttp
└── no_template (raw preserved, structured parsing skipped)
▸ Every command found in the log appears in JSON output — even commands without a template
▸ Platforms supported: cisco_nxos, cisco_ios (extensible via commands.yaml)
▸ Auto-discovery requires no YAML edit — just drop a template file in the right folder
▸ JSON output: one file per device, containing metadata + commands dict

## Slide 4
Running the Parser (main.py)
Installation & Quick Start
cd network_cli_parser
pip install -r requirements.txt
# Single .txt file
python main.py --input data/raw/N9K-CAMA-WAN-1_03-May-26.txt
# Entire directory (all .txt files)
python main.py --input data/raw/
# Custom output directory
python main.py --input data/raw/ --output /tmp/parsed/
Output
▸ One JSON file per input
▸ Written to data/json/ by default
▸ Filename: <hostname>_<date>.json
▸ Contains metadata + commands dict
▸ Raw output always preserved
JSON Snapshot Structure
{
"metadata": { "hostname": "N9K-CAMA-WAN-1", "platform": "cisco_nxos",
"collection_time": "2026-05-29T10:00:00" },
"commands": {
"show_version": { "status": "parsed", "raw": "...", "parsed": [{...}] },
"show_ip_bgp_summary": { "status": "parsed", "raw": "...", "parsed": [{...}] }
}
}

## Slide 5
Status Codes
Every command entry in the JSON carries one of these status values
Status | Meaning | Template Required?
parsed | Parser returned structured data rows | Yes
partial | Parser ran but returned 0 rows (template matched nothing) | Yes
raw_only | Explicitly registered as skip in commands.yaml | No (intentional)
failed | Parser threw an exception | Yes (broken template)
no_template | Not in registry; auto-discovery found nothing; raw preserved | Build one
How to handle no_template commands:
▸ The raw output is always preserved — nothing is lost
▸ Write a TextFSM or TTP template, drop it in templates/ — re-run and it auto-discovers
▸ Or add an explicit entry to commands.yaml pointing at the new template

## Slide 6
Adding a New Command
Three options — pick the one that fits your workflow
Option A — Explicit YAML registration
# commands.yaml
cisco_nxos:
show ip pim neigh:
parser: custom
template: cisco_nxos_show_ip_pim_neigh
Option B — Auto-discovery (no YAML edit)
# Drop the file in the right folder:
templates/custom/routing/
cisco_nxos_show_ip_pim_neigh.textfsm
# OR for TTP:
templates/ttp/routing/
cisco_nxos_show_ip_pim_neigh.ttp
# Auto-discovered on next run — no YAML edit!
Option C — Run first, build template later
▸ Run main.py with the new log — command appears as status: no_template
▸ Raw output is preserved in JSON — no data is lost
▸ Build a template, drop it in templates/ — re-run and it auto-discovers
Naming convention (auto-discovery):
Command: show ip pim neigh (cisco_nxos)
Normalized key: show_ip_pim_neigh
TextFSM: cisco_nxos_show_ip_pim_neigh.textfsm
TTP: cisco_nxos_show_ip_pim_neigh.ttp

## Slide 7
TextFSM Templates (parser: custom)
State-machine parser — ideal for tabular show outputs
Syntax
Value FIELD_NAME (regex)
Value Filldown VRF (\S+) # Carries forward across rows
Start
^header line regex -> Continue
^${FIELD}\s+${OTHER} -> Record
EOF
Key directives
Directive | Meaning
Value X (re) | Capture group, stored in field X
Filldown X (re) | Field carries forward until overwritten
-> Record | Emit current row to output
-> Continue | Re-process line in current state
EOF | Emit buffered row at end of input
Example — Multi-VRF PIM neighbor table
Value Filldown VRF (\S+)
Value NEIGHBOR (\d+\.\d+\.\d+\.\d+)
Value UPTIME (\S+)
Value STATE (\S+)
Start
^PIM Neighbor.*VRF\s+${VRF} -> Neighbors
Neighbors
^\s*${NEIGHBOR}\s+\S+\s+${UPTIME}\s+${STATE} -> Record
^PIM Neighbor.*VRF\s+${VRF} -> Continue.Record
EOF

## Slide 8
TTP Templates (parser: ttp)
Template Text Parser — ideal for hierarchical JSON output (VRF → neighbors)
Flat neighbor table
<group name="neighbors">
{{ neighbor_id }} {{ priority }}
{{ state | re("\\S+/\\s*\\S*") }}
{{ uptime }} {{ address }} {{ interface }}
</group>
Hierarchical (VRF → neighbors)
<group name="vrfs">
BGP summary for VRF {{ vrf }}, af {{ afi | re(".+") }}
BGP router identifier {{ router_id }}
<group name="neighbors">
{{ neighbor | re("\\d+\\.\\d+\\.\\d+\\.\\d+") }}
{{ remote_as }} {{ updown }} {{ state_pfx }}
</group>
</group>
Result JSON structure (hierarchical)
{ "vrfs": [{ "vrf": "default", "afi": "IPv4 Unicast", "router_id": "10.0.0.1",
"neighbors": [{ "neighbor": "10.0.0.2", "remote_as": "65002",
"updown": "2w3d", "state_pfx": "100" }] }] }
▸ Use re() when field contains spaces (e.g. FULL/ - would break default whitespace split)
▸ Use an IP-anchored regex on the first field to avoid accidentally matching header lines
▸ Naming: {platform}_{normalized_cmd}.ttp → cisco_nxos_show_ip_bgp_summary_vrf_all.ttp

## Slide 9
Pipe-Filtered Commands ( | include / | grep … )
Piped output has a different structure — it gets its own key and template
Normalization behaviour
Raw command | Normalized key
show ip bgp summary | show_ip_bgp_summary
show ip bgp summary ¦ include 65001 | show_ip_bgp_summary_include
show ip bgp summary ¦ exclude Connected | show_ip_bgp_summary_exclude
show ip route ¦ begin 10.0.0 | show_ip_route_begin
show ip route ¦ grep 10.0.0 | show_ip_route_grep
show ip route ¦ count | show_ip_route_count
Template file naming (auto-discovered):
# TextFSM (drop in templates/custom/):
cisco_nxos_show_ip_bgp_summary_include.textfsm
# TTP (drop in templates/ttp/):
cisco_nxos_show_ip_bgp_summary_include.ttp
# No YAML edit needed — auto-discovered
Explicit YAML registration:
cisco_nxos:
show ip bgp summary | include:
parser: custom
template: cisco_nxos_show_ip_bgp_summary_include
# Note: use the literal '| include' as the key
# The mapper normalizes it at load time

## Slide 10
Report Generator (report.py)
Operates on JSON snapshots; supports JSON + self-contained HTML output
Subcommand | Purpose | Output
delta | Field diff between two snapshots | JSON / HTML
delta-all | Per-device delta across two directories | HTML + index.html
health | YAML check file vs single snapshot | JSON / HTML (exit 1 on critical fail)
health-all | Health checks across all snapshots in a dir | Single combined HTML report
baseline | Auto-generate starter check YAML from current values | YAML file
collect | Collect via SSH (online) or process .txt dumps (offline) | JSON snapshots
Common invocations
python report.py health --snapshot data/json/N9K.json --checks checks/base.yaml
python report.py health --snapshot data/json/N9K.json --checks checks/base.yaml --output health.html # → health.html + health_simple.html (default)
python report.py health-all --dir data/json/ --default-checks checks/base.yaml --output-dir reports/
python report.py delta --before before/N9K.json --after after/N9K.json --output delta.html
python report.py delta-all --before-dir snapshots/03-May/ --after-dir snapshots/04-May/ --output-dir reports/
python report.py baseline --snapshot data/json/N9K.json --output checks/baseline.yaml
python report.py collect --from-dir data/raw/ --output-dir data/json/

## Slide 11
Health Check — Path Syntax
Paths navigate the parsed JSON structure of a command
Token | Meaning
[0] | Index into a list → first element
[*] | Expand ALL items of a list OR all values of a dict
.field | Access a dict key (dot is optional at start of path)
field | Dict key at the start of a path (no leading dot needed)
Examples
Path | What it accesses
[0].os | First element of a list, os field
[*].status | status field from every row in a list
vrfs[*].summary.total_routes | total_routes from summary of every VRF in a dict
neighbors[*].state | state from every neighbor in a list
goid[*].peer[*].ike_status | ike_status from every peer inside every GOID
When [*] expands multiple values → condition is checked against each one (all must pass by default; use match: any to require at least one)

## Slide 12
Conditions — 14 Built-in Operators
Use the condition field in a check definition
Condition | Passes when (actual vs expected)
eq | actual == expected
ne | actual != expected
gt / gte | actual > / >= expected (numeric)
lt / lte | actual < / <= expected (numeric)
contains | str(actual) contains expected substring
not_contains | str(actual) does NOT contain expected substring
matches | str(actual) matches expected regex (re.search)
one_of ★ | actual is in the expected list → value: [a, b, c]
not_one_of ★ | actual is NOT in the expected list
duration_gt / duration_gte | parsed duration > / >= expected duration
duration_lt / duration_lte | parsed duration < / <= expected duration
★ one_of / not_one_of are new — see slide 16 for full examples | Duration conditions parse strings like '5w2d', '00:03:42', 'never'

## Slide 13
Duration Conditions
Compare uptime / timer strings without manual string parsing
Supported input formats
Input | Interpreted as
5w2d | 5 weeks + 2 days
2d03h | 2 days + 3 hours
1y3w2d4h5m6s | full decomposition
00:03:42 | HH:MM:SS
15:30 | MM:SS
5week2day | spelled-out units
never / n/a / - | 0 seconds
42 | 42 seconds (bare integer)
Example checks
# BGP session up at least 2 days
- name: "BGP session stable"
command: show_ip_bgp_summary_vrf_all
path: "vrfs[*].neighbors[*].updown"
condition: duration_gte
value: "2d"
# OSPF neighbor up more than 1 week
- name: "OSPF neighbor stable"
command: show_ip_ospf_neighbors
path: "neighbors[*].uptime"
condition: duration_gt
value: "1w"
# PIM neighbor recently reset (< 1h)
- name: "PIM neighbor fresh"
command: show_ip_pim_neigh
path: "[*].UPTIME"
condition: duration_lt
value: "1h"
▸ Both actual (from snapshot) and value (from YAML) go through the same parser
▸ Use any supported format in either field — they don't need to match
▸ 0 is NOT > 0 — 'never' fails duration_gt: '0s'

## Slide 14
match and severity Fields
Control how multi-value expansion is evaluated + how failures affect CI
match: all / any
match value | Default? | Passes when
all | Yes | Every expanded value satisfies the condition
any | No | At least one expanded value satisfies the condition
# At least one IKE peer is Established
- name: "IKE peer alive"
command: show_crypto_gkm_ks_coop_detail
path: "goid[*].peer[*].ike_status"
condition: matches
value: "Established"
match: any # pass if ANY peer is Established
severity: critical / warn / info
severity | Default? | Exit code on failure
critical | Yes | exit 1 — blocks CI
warn | No | exit 0 — shown in report only
info | No | exit 0 — informational
# MTU mismatch is a warning, not a blocker
- name: "MTU is jumbo"
command: show_interfaces
path: "[*].mtu"
condition: eq
value: 9216
severity: warn
# Baseline checks default to warn so they
# never block CI until explicitly promoted
Both match and severity are optional — omitting them uses the defaults (all / critical)

## Slide 15
★ AND Conditions (New) — conditions list
All conditions in the list must pass for each resolved value
Use case: range checks — value must be > min AND < max
# BGP prefix count must be between 1 and 500,000 (both bounds must hold)
- name: "BGP prefix count in valid range"
command: show_ip_bgp_summary
path: "neighbors[*].prefixes_received"
conditions: # ← list replaces single condition/value
- condition: gte
value: 1
- condition: lte
value: 500000
severity: critical
# Works with match: any too
- name: "At least one interface has valid MTU"
command: show_interfaces
path: "[*].mtu"
conditions:
- condition: gte
value: 1500
- condition: lte
value: 9216
match: any
How it works
▸ Each item in conditions has its own condition + value
▸ An item passes only if ALL conditions pass (AND logic)
▸ On failure, every failing sub-condition is listed separately
▸ Compatible with match: all (default) and match: any
▸ Cannot combine conditions with branches in the same check
Failure output (terminal)
✗ BGP prefix count [fail]
path: neighbors[0].prefixes_received
actual: 600000
reason: 600000 not <= 500000

## Slide 16
★ one_of and not_one_of (New)
Value must be in (or not in) a list of allowed values
one_of — value must be in list
# Interface protocol must be 'up' or 'connected'
- name: "Interface protocol valid"
command: show_interfaces
path: "[*].line_protocol"
condition: one_of
value: ["up", "connected"]
# BGP state must be Established or Active
- name: "BGP peer state acceptable"
command: show_ip_bgp_summary
path: "neighbors[*].state_pfx"
condition: one_of
value: ["Established", "Active", "Idle"]
severity: warn
not_one_of — value must NOT be in list
# No interface description should be DECOM
- name: "No decom interface"
command: show_interfaces
path: "[*].description"
condition: not_one_of
value: ["DECOM", "DECOMMISSIONED", "DELETE"]
# Spanning tree state — block bad states
- name: "No STP blocking"
command: show_spanning_tree
path: "[*].port_state"
condition: not_one_of
value: ["BLK", "discarding"]
severity: warn
Key points
▸ value must be a YAML list [item1, item2, ...] — a plain string value causes an error
▸ Works with match: all (default) or match: any — e.g. require at least one interface to be up
▸ Combines with severity: warn/info to make non-blocking checks

## Slide 17
★ Conditional Branches IF / ELIF / ELSE (New)
Apply different checks depending on a field value in each row
Syntax
- name: "MTU matches interface type"
command: show_interfaces
path: "[*]" # must resolve to dict rows
branches:
- when: # IF
field: type
condition: eq
value: loopback
then:
field: mtu
condition: eq
value: 65535
- when: # ELIF
field: type
condition: contains
value: Ethernet
then:
field: mtu
condition: eq
value: 9216
- default: # ELSE
field: mtu
condition: gte
value: 1500
How it works
▸ path must resolve to dict rows
▸ when: field/condition/value is the IF guard
▸ Branches are evaluated in order — first match wins
▸ default fires if no when matched (ELSE)
▸ No match + no default → row passes vacuously
▸ Non-dict row → fail with type error
▸ Compatible with match: all / any
▸ Compatible with print field
then / default structure
then: # or default:
field: mtu # field to evaluate in the row
condition: eq # any standard condition
value: 9216 # expected value

## Slide 18
★ print Field (New) — Surface Values in Output
Display resolved values on every check — pass or fail
Two forms
# print: true — raw path → value
- name: "Current OS version"
command: show_version
path: "[0].version"
condition: matches
value: "17\\..*"
print: true
# Terminal output:
# ✓ Current OS version [pass]
# [0].version -> '17.6.1a'
# print: "template" — compose a sentence
- name: "BGP prefix count"
command: show_ip_bgp_summary
path: "neighbors[*].prefixes_received"
conditions:
- {condition: gte, value: 1}
- {condition: lte, value: 500000}
print: "Peer {path} has {value} prefixes"
# Terminal output per peer:
# Peer neighbors[0].prefixes_received has 12453 prefixes
Template placeholders
Placeholder | Replaced with
{value} | The resolved actual value (str)
{path} | The resolved path string e.g. neighbors[0].state
Works with all check types
▸ Simple checks (condition + value)
▸ AND checks (conditions list)
▸ Branches (when/then/default)
▸ Shown on BOTH pass and fail
▸ One printed line per resolved item
▸ Also rendered in HTML report
# print with branches
- name: "MTU by type"
command: show_interfaces
path: "[*]"
print: "Interface {path} MTU is {value}"
branches:
- when: {field: type, condition: eq, value: loopback}
then: {field: mtu, condition: eq, value: 65535}
- default: {field: mtu, condition: gte, value: 1500}

## Slide 19
Compound Conditions — Full Example
Combining conditions, branches, print, match, and severity in one check file
checks:
# AND conditions — range check
- name: "BGP prefix count in range"
command: show_ip_bgp_summary
path: "neighbors[*].prefixes_received"
conditions:
- condition: gte
value: 1
- condition: lte
value: 500000
print: "Peer {path} has {value} prefixes"
severity: critical
# one_of — valid protocol states
- name: "Interface protocol valid"
command: show_interfaces
path: "[*].line_protocol"
condition: one_of
value: ["up", "connected"]
match: all
severity: critical
# not_one_of — no decom interfaces
- name: "No DECOM interface"
command: show_interfaces
path: "[*].description"
condition: not_one_of
value: ["DECOM", "DECOMMISSIONED"]
severity: warn
# Branches IF/ELIF/ELSE — MTU by interface type
- name: "MTU matches interface type"
command: show_interfaces
path: "[*]"
print: "Interface {path} MTU={value}"
branches:
- when: {field: type, condition: eq, value: loopback}
then: {field: mtu, condition: eq, value: 65535}
- when: {field: type, condition: contains, value: Ethernet}
then: {field: mtu, condition: eq, value: 9216}
- default: {field: mtu, condition: gte, value: 1500}

## Slide 20
Per-Device Check Overrides & Baseline Generation
Two-tier check system: default checks + per-device overrides
Per-device override file
# checks/devices/N9K-CAMA-WAN-1.yaml
checks:
# OVERRIDE: replaces default check (same name)
- name: "VPC peer link status is up"
command: show_vpc_brief
path: "[*].status"
condition: not_contains
value: "peer-link down" # more permissive
# ADDITION: only for this device
- name: "Hostname matches expected"
command: show_version
path: "[0].hostname"
condition: eq
value: "N9K-CAMA-WAN-1"
# Merge rule: device check WINS on name clash
# All other default checks remain unchanged
CLI usage
# Single device with override
python report.py health \
--snapshot data/json/N9K.json \
--checks checks/base.yaml \
--device-checks checks/devices/N9K.yaml
# All devices — auto-loads {hostname}.yaml
python report.py health-all \
--dir data/json/ \
--default-checks checks/base.yaml \
--device-checks-dir checks/devices/ \
--output-dir reports/health/
Auto-baseline generation
python report.py baseline \
--snapshot data/json/N9K.json \
--output checks/baseline_N9K.yaml
# Generates eq checks for every scalar field
# Default severity: warn (won't block CI)
# Review and promote critical ones manually
▸ File naming: checks/devices/{hostname}.yaml — loaded automatically in health-all
▸ Devices with no matching file use only the default checks

## Slide 21
Delta Report — Field-Level Diff Between Snapshots
Natural-key row matching — position changes are not reported as diffs
Natural key priority
Natural key tried (in order) | Example
INTERFACE / interface / port | Interface tables
NEIGHBOR / neighbor / neighbor_id | BGP / OSPF neighbor tables
NETWORK / PREFIX / network | Route tables
VLAN / vlan_id | VLAN tables
Index (fallback) | Any other list
JSON output structure
{
"metadata": {
"before": {"hostname": "...", "collection_time": "..."},
"after": {"hostname": "...", "collection_time": "..."}
},
"summary": {
"commands_added": ["cmd_a"],
"commands_removed": [],
"commands_changed": ["show_vpc_brief"],
"commands_unchanged": ["show_version", "..."]
},
"changes": {
"show_vpc_brief": {
"diffs": [
{
"path": "parsed[port=Po10].status",
"before": "up",
"after": "down"
}
]
}
}
}
▸ Row moving position in a list is NOT reported — only genuine field value changes are
▸ Commands present in only one snapshot appear as added / removed
▸ delta-all matches devices across directories by metadata.hostname

## Slide 22
HTML Reports — Health & Delta
All CSS and JS embedded; fully self-contained .html files — no internet required
Single-device health report layout
Section | Description
Summary cards | Total / Passed / Failed / Errors at a glance
Check results | Color-coded card per check; failures show path, actual, reason
Severity badges | WARN / INFO badges on non-critical failures
Printed values | Rendered per-item printed list (pass and fail)
Raw CLI outputs | Every command's raw text; Expand All / Collapse All
Parsed JSON outputs | Structured parsed data per command; independent Expand All
Delta report layout
Section | Description
Metadata | Before → After hostname and timestamp side by side
Summary cards | Added / Removed / Changed / Unchanged
Added / removed | Command names as pills
Changed commands | Diff table: path / before (red) / after (green)
Raw outputs | Changed commands: before + after side by side
delta-all index page
Column | Notes
Hostname / Status | matched → link to delta HTML; unmatched → faded, no link
Added / Removed / Changed / Unchanged | counts from compute_delta() summary
Row style | Muted green-tint if zero changes; faded grey if unmatched device
Devices appearing in only one directory (delta-all) are listed as UNMATCHED with no report link.
health / health-all generate a second health_simple.html by default — pass/fail only, no raw CLI or config values, safe to forward to management. Control with --report-mode both|detailed|simple.

## Slide 23
Combined Health-All Report (health_report.html)
One file covers all devices — check × device matrix at the top, full detail per device below
Report structure
Section | Description
Summary cards | Devices / Total check evals / Passed / Failed / Errors
Check × device matrix | Row per check, column per device — cells PASS / FAIL / ERR / —
Cell colour-coding | Green = pass · Red = fail · Amber = error · Grey = absent
Matrix cell links | Click any cell → page jumps to that device's accordion
Per-device accordions | Click device name → expands full detail inline
Accordion: checks | Full check result list with pass/fail/warn badges
Accordion: raw CLI | All command raw outputs with Expand All / Collapse All
Accordion: parsed JSON | Structured JSON per command; independent Expand All
CLI invocation
# Minimal — HTML only
python report.py health-all \
--dir data/json/ \
--default-checks checks/base.yaml \
--output-dir reports/health/
# → reports/health/health_report.html # → reports/health/health_report_simple.html
# With per-device JSON files as well
python report.py health-all \
--dir data/json/ \
--default-checks checks/base.yaml \
--device-checks-dir checks/devices/ \
--output-dir reports/health/ \
--format both
# → health_report.html + {hostname}_health.json
Key behaviours
▸ Single HTML — no per-device files, no index.html
▸ Device-specific YAML (--device-checks-dir) overrides default checks by name
▸ Exit code 1 if any critical check fails across any device
▸ Matrix columns truncated at 15 chars with full name in tooltip
▸ Raw CLI and Parsed JSON toolbars are independent (separate JS functions)
▸ --report-mode both (default) also writes health_report_simple.html — executive dashboard with pass/fail only, no raw output or config values

## Slide 24
Snapshot Collector (report.py collect)
Full pipeline: from live device to JSON snapshot — no main.py call needed
Offline mode (no SSH needed)
# Process existing .txt CLI dumps
python report.py collect \
--from-dir data/raw/ \
--output-dir data/json/
# Same parsing pipeline as main.py
SSH mode (requires pip install netmiko)
python report.py collect \
--devices devices.yaml \
--raw-dir data/raw/ # optional .txt dumps
--output-dir data/json/ \
--password <pw>
devices.yaml format
defaults:
username: admin
password: "" # leave blank, use --password
timeout: 30
devices:
- hostname: N9K-CAMA-WAN-1
host: 192.168.1.1
platform: cisco_nxos
- hostname: IOS-RTR-1
host: 10.0.0.1
platform: cisco_ios
username: ops # override defaults
- hostname: N9K-CAMA-WAN-2
host: 192.168.1.2
platform: cisco_nxos
commands: # explicit list (overrides registry)
- show version
- show ip bgp summary vrf all
End-to-end workflow:
python report.py collect --devices devices.yaml --output-dir data/json/
python report.py delta-all --before-dir data/json-prev/ --after-dir data/json/ --output-dir reports/delta/
# Produces reports/delta/{hostname}_delta.html + reports/delta/index.html
python report.py health-all --dir data/json/ --default-checks checks/base.yaml --output-dir reports/health/
# Produces single reports/health/health_report.html (matrix + per-device accordions)

## Slide 25
Network CLI Structured Parser
Quick Reference Card
▸ main.py → Parse .txt dumps to JSON (data/json/)
▸ report.py collect → SSH or offline batch collection
▸ report.py health → YAML checks against snapshot (exit 1 on critical fail)
▸ report.py delta → Field-level diff between two snapshots
▸ report.py baseline → Auto-generate starter check YAML
▸ Compound checks: conditions (AND) · one_of / not_one_of · branches (IF/ELIF/ELSE)
▸ print field: surface resolved values in terminal + HTML on pass and fail
▸ match: any — at least one value must pass; severity: warn/info — no CI block
Full reference: PARSER_SOP.md | Starter checks: checks/example_health_checks.yaml

## Slide 26
★ Executive Health Dashboard — --report-mode (New)
health and health-all now generate a management-safe simple dashboard alongside the full report
Default output (--report-mode both)
health.html
Full detailed report
Raw CLI output, parsed JSON,
conditions & actual values
health_simple.html ★
Executive dashboard
Pass/fail badge per check
Failure count only ("3 of 5 failed")
No IPs, no config values
Safe to forward to management
CLI — --report-mode flag
# Default — both files generated
python report.py health \
--snapshot N9K.json \
--checks base.yaml \
--output health.html
# Management-only (no detail)
python report.py health \
--output health.html \
--report-mode simple
# Engineers only (old behaviour)
--report-mode detailed
--report-mode | Files written | Use case
both (default) | health.html + health_simple.html | Engineers get full detail; management gets clean summary
detailed | health.html only | Engineers only — original pre-feature behaviour
simple | health_simple.html only | Management forwarding — minimal data exposure risk